## Slide 1: Air-sea Fluxes: BOMEX to EUREC4A/ATOMIC C.W. Fairall NOAA Jim Edson, Frank Bradley, Jeff Hare, Sergio Pezoa, Ludovic Bariteau, Byron Blomquist
What are fluxes?
Why do we want fluxes?
Measurement
Issues
BOMEX
Modern

## Slide 2: Fluxes In General
Budget equation for variable x=X+x’
Rate change = [ turbulent + molecular + mean fall + slip covariance+ Source]
<w’x’> turbulent transport
Source Examples:
Temperature – radiative flux, condensation
Water vapor – evaporation
Liquid water – condensation, sea spray
Ozone – chemical reactions in air or water, e.g. Qx=-CxyXY
Particles – gas-particle, coalescence, sea spray, blowing dust, meteors
Volume source becomes an area flux

## Slide 3: Applications for Surface Fluxes
A few examples
Model lower boundary conditions (LES, PBL, Mesoscale, NWP, GCM)
Ocean budgets (stress, heat, waves, sea-ice)
Carbon budgets (uptake CO2 by oceans)
Pollution deposition (particle, ozone)
Cloud microphysics (aerosol source, DMS source of sulfur)
Hurricane intensity
Global warming

## Slide 4: Turbulent Flux Definitions
Surface Energy and Mass Budgets

## Slide 5: Surface Turbulent Flux Parameterizations
Turbulent Fluxes: Parameterization using U, Ts, T, etc.
Flux= Mean correlation of turbulent variables, <w’x’>
MetFlux – Dominated by atmospheric turbulent transfer physics
GasFlux – Dominated by oceanic molecular transfer physics;
Enhanced by whitecap bubbles
Transfer coefficients computed from direct flux measurements

## Slide 6: Community Flux Products Using Bulk Estimates
NWP: SURFA Archived flux fields from ECMWF, DWD, JMA
Blended: WHOI OAFlux, CORE,..
Satellite: SEAFLUX, GSSTF, HOAPS, JOFURO, IFREMER

## Slide 7: Measurement Near-Surface Turbulent Fluxes <w’x’>
Sensors (w’, x’)
  10 Hz, 3 digit resolution, 2.5% accuracy, withstand marine environment
Platform
  Ship, buoy, aircraft, pier, ocean- or land-based tower
Processing
  Fast DAS, time synchronization, high pass filtering (x=X+x’), averaging, motion corrections, coordinate transform
Dirt effects
  Sensor crosstalk, Sea salt and biochemical, ship effluent, radio/radar interference, flow distortion, flow distortion, birds
Ancillary
  All variables relevant to parameterization, platform navigation, food

## Slide 8: BOMEX Research Vessel with Flux Sensors

## Slide 9: Floating Instrument Platform FLIP World’s Largest Spar Buoy

## Slide 10: BOMEX Platforms: Land and Air
NOAA DC-6
Tower on Barbados

## Slide 11
BOMEX vs Modern |  | 
 | BOMEX | EUREC4A/ATOMIC
Flux Platforms | Ships, FLIP, 2 A/C, Tower | 4 ship, 4 A/C, UAS, UAV
u’, v’, w’ | Sonic anemometer, gust vanes, propellers, hot wire anemometer | Sonic anemometer, 5-hole pressure ports
T’ | Microthermal wires | Sonic anemometer, Microthermal (UAS)
q’ | 1 channel UV absorption, wet/dry bulbs | 3-channel IR absorption
Motion | FLIP (cheating), INS | IMU (combined accelerations/GPS)
sonic
Rain gauge
IR hygrometer
T/RH
motion
Lidar wave gauge

## Slide 12: BOMEX Latent Heat Flux Estimates
6 mm/day = 173 W/m^2

## Slide 13: 10-m Evaporation Coefficient
Humidity and heat 10-m transfer coefficients. Average 20,300 observations. Uconn – Hs; PSD – Hl.
Post BOMEX
Fairall et al. 2011

## Slide 14
‘You cannot measure fluxes from a ship’ quote from a famous tropical meteorologist
HIWINGS 2013
SeaState 2015

## Slide 15: Improved in situ air-sea flux observations
1974
2005

## Slide 16: ‘You cannot measure fluxes from a ship’ - a famous tropical meteorologist
Stress observations
HIWINGS field program South of Greenland November 2015.
Covariance measurements vs two versions of COARE model