## Slide 1: Réunion de la Plateforme OCAPI de l’IPSL Mesures de GES en IDF Irène Xueref-Remy OHP/OSU Pytheas
18 septembre 2017
IPSL Jussieu Salle Darcy Tour 46-56 / 3ème étage

## Slide 2: Scientific context and objectives
Large uncertainties on the inventories of anthropogenic emissions at the regional scale
+70% CO2 FF = zones urbanisées/industrialisées
Mean CO2 budget 2006-2015
(Le Quéré et al, 2016)
Peylin et al, 2001, 2013
Large uncertainties on the carbon sinks
at the regional scale
25% ± 5%
30% ± 8%
45% ± 1%
FF: 91,3% ± 4,5%
BB: 9,7% ± 4,8%
Sinks
Increase of atmospheric CO2
Understanding the carbon cycle at the Anthropocene era :
Regional sources and sinks, impacts on ecosystems and helping policy makers for emissions mitigation
Acidification
Species endangering
Fertilization
T increase / hydric stress

## Slide 3
The carbon budget is highly uncertain at the continental, regional and local urban scales
Source : LSCE, ICOS-Fr and ICOS-ATC teams
High spatio-temporal atmospheric CO2 variability, mostly over continents.
Reflects the variability of the CO2 fluxes exchanged between the Earth surfaces and the atmosphere.
Understanding the carbon cycle at the Anthropocene era
2- Scientific context and objectives
Atmospheric CO2 concentration (ppm)
Notes: ALLER TRES VITE VERS LA FIGURE POUR NE PAS PERDRE DE TEMPS!
- Ce budget, ici donné à l’échelle globale, est très incertain aux échelles continentale, régionale et plus locales : c’est en effet difficile de réduire ces incertitudes,
car beaucoup de processus entrent en jeu.
- Je vous montre sur cette figure les séries temporelles du CO2 atmosphérique collectées dans les stations
du réseau ICOS-FR qui a développé des stations d’observations en France mais aussi à l’international.
- On peut voir ici que, hormis l’augmentation globale à long-terme de l’ordre de 2 ppm/an observée pour toutes les stations, la variabilité du CO2 atmosphérique
est très différente en fonction de l’endroit du globe où l’on collecte les mesures.
- Par exemple, cette variabilité est quasi-nulle à l’Ile Amsterdam dans l’Océan Sub-Antarctique car les échanges de CO2 sont contrôlés pour la plupart dans l’océan de surface. - Alors que sur les continents, la variabilité du CO2 atmosphérique est beaucoup plus élevée, comme on peut le voir ici sur la courbe verte enregistrée au Puy-de-Dôme où le cycle saisonnier
de la biosphère liée aux processus de photosynthèse et de respiration modulent la concentration du CO2 atmosphérique.
- Enfin, si l’on se rapproche des zones urbanisées comme ici à Saclay, on peut voir se rajouter des pics de concentration assez marqués qui proviennent des émissions de CO2 de la
mégapole parisienne et ne sont pas encore bien mélangées dans l’atmosphère.
- Ainsi, cette variabilité reflète en partie celle des flux de CO2 échangés entre les surfaces terrestres et l’atmosphère.

## Slide 4
2009
Paris
ANR blanc CO2-MEGAPARIS
(PI: I. Xueref-Remy)
Urbanized and industrialized areas (UIAs) = more than 70% of CO2FF emissions.
UIAs’ inventories uncertain => need independent verification: this can be down through atmospheric approaches.
Major socio-political stakes (Cities Climate Energy Plans).
2010
Indianapolis
NIST INFLUX 2010
(PI: Paul Shepson)
2010
Los Angeles
NASA MEGACITIES
(PI: R. Duren)
The international context in 2009-2010 : focus on CO2 emissions from megacities

## Slide 5: Du développement d’un réseau d’observation régional pour étudier le panache de CO2 parisien et l’inventaire d’émissions total à une approche multi-espèces pour identifier les secteurs d’émissions de CO2 en IDF
CO2-MEGAPARIS (ANR blanc, PI)
ASTRE (CG Essonne, PI)
MULTI-CO2 (IPSL, PI)
Le CO2 parisien (Ville de Paris, PI)
La Plateforme OCAPI (IPSL)
2009
2016
2011
2012
2013
2014
2015
2010
2017
CARBOCOUNT-CITY (KIC Clim, PI adj.)

## Slide 6: Question 1: How uncertain are the Paris region CO2 emission inventories?
Postdoc. Elsa Dieudonné (2011-2012)
Dieudonné et al, AGU 2013 ; Dieudonné et al, CO2-MP report, 2012 ; Dieudonné et al, in prep)
=> We need to develop atmospheric « top-down » approaches to assess the Paris megacity CO2 emissions inventories independently.
A detailed study (spatial and temporal fine scales) can be found in Dieudonné et al, CO2-MP report, 2012.
Sectoral mismatch (IER-AirParif):
Differences on total emissions:
Airparif (AP): 52.1 MtCO2/yr
IER: 62.9 MtCO2/yr
Relative difference :
20.7 %
Intercomparison of AIRPARIF (Paris) and IER (Stuttgart) HR inventories (1x1 km2, 1h, 2008)
Relative difference (%)
Chart: 
| Traffic | Residential | Tertiary | Industry
 | 30.6407 | -9.3106 | -62.4041 | 48.8889
Traffic
+30.6 %
Residential
-9.3%
Tertiary
-62,4 %
Industry
+ 48.9 %
(IER-AP)/[1/2x(IER+AP)]
« Bottom-up » approach:
Es : Total emissions of each activity sector (ex. traffic)
Fi: Emission factor (benchmarks – ex. gCO2/km)
Ai: Activity rate (statistics databases – ex. number of kilometers travelled)
Pi = activity parameter (ex. catalyst vehicle or not)
Es = S Ai x Fi x Pi
with i : category (ex. two wheels vehicles)
Notes: La première question que je me suis posée…
J’ai organisé….
Les inventaires d’émissions sont construits sur une approche dite « montante », basés pour chaque secteur et chaque catégorie de ce secteur sur la somme du produit d’un proxy d’activité (Ai),
d’un facteur d’émission Fi et d’un paramètre d’activité Pi correctif (ex. équipement des véhicules avec des pots catalytiques).
Les proxies d’activités proviennent généralement de statistiques économiques, tandis que les facteurs d’émissions et paramètres d’activités sont mesurés sur bancs d’essai, mais pas dans la vie réelle:
par exemple, l’état des roues du véhicules, ou l’état du revêtement des routes n’est pas pris en compte. Cela explique pourquoi les inventaires d’émissions sont d’une manière générale très incertains.
Pour le cas de Paris, il existe donc deux inventaires d’émissions à haute résolution : IER et AIRPARIF. Sur le total émis, la différence relative est de 20,7%. Les différences sont encore
plus fortes quand on les calcule pour chacun des secteurs d’émissions, notamment pour le trafic où l’on dépasse les 30% de différence, le secteur industriel avec près de 50% d’écart
et le secteur du chauffage tertiaire avec plus de 60% d’écart.
Une étude détaillée…

## Slide 7
Xueref-Remy et al, 2016
Question 2 : Can we observe an atmospheric CO2 plume from Paris megacity?
Development of the Paris in-situ CO2 network
Co-workers:
Cyrille Vuillemin (CO2-MP Engineer, 1 year)
Elsa Dieudonné (CO2-MP postdoctorate)
Martina Schmidt, Marc Delmotte & the RAMCES (ICOS) team
AIRPARIF
François Ravetta (QUALAIR) & Martial Haeffelin (SIRTA)
CO2 CO2-MP
CO2 ICOS
Aerosols LIDARs (TRN’s = CO2-MP/ICOS)
EIF -
Urban
GIF – Peri-urban
MON -Rural
GON – Peri-urban
SW
NE
TRN -
Rural
G1302
Notes: Détecter et quantifier le panache parisien
Support aux travaux de modélisation directe et inverse

## Slide 8
Days in March 2011
500
480
460
440
420
400
380
CO2 concentration (ppm)
1400
1200
1000
800
600
400
200
ABL height (m AGL)
EIF: 317 m AGL
Days in March 2011
Question 2 : Can we observe an atmospheric CO2 plume from Paris megacity ?
Analysis at the diurnal, synoptic and seasonal scale
Hour (UTC)
Detailed driving factors analysis in Xueref-Remy et al (in rev): hABL, surface fluxes, wind speed & direction, time.
Gradient between stations: 1 to 25 ppm=> Regional impact of Paris megacity activities on atmospheric CO2.
Xueref-Remy et al, 2016, in rev. for ACP
430
420
410
400
390
CO2 concentration (ppm)
Ex. Diurnal cycles
0 5 10 15 20
4 Aug.2010
13 July 2011
Date
EIF
380
500
[CO2] (ppm)
Hourly average over ~1 year

## Slide 9
Sept Nov Jan Mar Apr Jul
Sept Nov Jan Mar Apr Jul
GON minus GIF
GIF minus GON
Paris megacity CO2 plume (ppm)
25
20
15
10
5
0
-5
25
20
15
10
5
0
-5
Xueref-Remy et al, AGU 2015
Xueref-Remy et al, in prep
Question 2 : Can we observe an atmospheric CO2 plume from Paris megacity?
430
420
410
400
390
380
370
Sept Nov Jan Mar Apr Jul
SW GIF
SW TRN50
SW TRN180
MHD
430
420
410
400
390
380
370
CO2 concentration (ppm)
NE GON
NE MON
MHD
Sept Nov Jan Mar Apr Jul
Background concentration : from upwind stations (ex.seasonal scale)
Extracting the Paris megacity atmospheric CO2 plume (ex.seasonal scale)
LESSONS / CO2 URBAN PLUMES:
Synoptic background variability
as large as the Paris CO2 plume
MHD is too far
OK=Regional site, city upwind
See also Turnbull et al, 2015
Wind selection required:
3-8 m.s-1
30° cones (ie +/-15°)
Afternoon hours only
FLEXPART backplumes
(Lopez et al, 2013)
EDGAR 2010

## Slide 10
Stage M2 Lamia Ammoura
Postdoct. Sandip Pal
Lidar intensive campaign : 21-25 mars 2011 (collab. LSCE/LATMOS-QUALAIR/LMD-SIRTA)
Observed UHI :
Observed ABL height gradient due to UHI :
20
15
10
5
0
Temperature (°C )
21/03 22/03 23/03 24/03
We demonstrated that the UHI observed over the Paris megacity generated a ABLh regional gradient:
Urban vs peri-urban sites: Daytime = + 6 % / Nighttime = 45 %
Urban vs rural sites : Daytime = +19% / Nighttime: NA
Question 3 : Impacts of the urban heat island (UHI) on the ABL height
(a key factor in CO2 emissions dilution in the atmosphere) ?
Pal et al, ACP 2012
JUSSIEU (urban)
=> Ceilometer
=> Lidar
TRAINOU (rural)
SIRTA (peri-urban)

## Slide 11
CO2 (ppm)
Altitude (m ASL)
580
560
540
520
500
480
460
440
420
400
1000
900
800
700
600
500
400
300
200
100
0
Inverse modeling studies, that allowed us to improve the AirParif inventory (EXTRA SLIDE) Bréon et al, ACP 2015 ; Staufer et al, ACP 2016
EIF
8h UTC
11h UTC
Question 4 : Assessing the performances of a URBAN transport modeling framework
Collaboration with CNRM (C. Lac, V. Masson et al)
Lac et al, ACP 2013
The TEB model improves the matching to observations and is required for urban and peri-urban sites
The MESO-NH framework well reproduces the phasing of the ABL height, which is a very important point at EIF.
REF : with TEB / RUR : without TEB
ABL height (m AGL)
EIF
Direct modeling with MESO-NH coupled with the TEB urban canopy model at HR (2 x 2 km2, 1 h)

## Slide 12
Question 5 : Assessing the role of the different emission sectors on urban atmospheric CO2 ?
=> Developping a multi-species approach
14C (radiocarbon) :
13C (stable isotope) :
Carbon isotopes
No 14C in CO2FF
Coal
-24.0
Biosphere
-24.7
Oil
-28.9
Natural gas
-39.1
d13C (‰)
FF: Widory et al, PARIS 2003 ; Bio: Bakwin et al, 1998
-8.0
Atmosphere
Species co-emitted with anthropic CO2 (ex. of Paris)
PMF approach (Positive Matrix Factorization)
=> COVs emission profile for each source (ex. traffic)
Adapted from Gaimoz et al, 2011)
COVs
Quantité de l’espèce (%)
25
20
15
10
5
0
Traffic
Airports
Wastes
Energy
Residential& tertiary
Industry
Constructions & quarries
Agriculture
Complete combustion
Incomplete combustion
5%
43%
29%
7%
4%
4%
7%
1%
5%
CO2FFeq
Traffic (exhaust)
Fuel evaporation
Wood burning
Solvants
Natural gas
Local source
Biogenic source
soot…

## Slide 13
14CO2 and 13CO2 winter campaign (ANR CO2-Megaparis / EU MEGAPOLI collaboration)
Isotopic analysis in the Paris atmosphere in Winter 2010 (LHVP, Paris 13th district):
25% CO2BIO: Human & biogenic respirations, biofuels combustion
75% CO2FF :
Limitations :
Study valid in wintertime only
Use of a continental background for CO2 and 14CO2 (MHD), not regional.
Unknown uncertainties due to the source signatures:
d13C biosphere poorly known
d13C signature of fossil fuels variable depending on their origin (Andres et al, 2000)
PhD work of Morgan Lopez (2009-2012)
Natural gas: 70%
Oil: 30%
Lopez et al, ACP 2013
Principal investigator of this campaign : Martina Schmidt (ICOS-Fr team)
In agreement with AIRPARIF inventory
Question 5 : Assessing the role of the different emission sectors on urban atmospheric CO2
=> Can we move on further by using VOC measurements?

## Slide 14
PhD work of Lamia Ammoura (2012-2015)
Collaboration with Jean Sciare, Valérie Gros, Bernard Bonsang (CAE) & Frédéric Chevallier (SatInv)
Tunnel campaign at the Fall 2012 (ADEME Primequal ZAPA project)
Characterizing atmospheric CO2-COVs correlations for traffic only
z
CO
NOx
Benzene
Dspecies/DCO2 (traffic)
Toluene
MKP-Xylenes
n-Xylenes
n-propylbenzene
n-ethylbenzene
acetylene
propene
ethylene
i-pentane
n-pentane
Ammoura et al, ACP, 2014
We inferred that the COVs matrix of speciation of the AIRPARIF inventory must be updated.
Our study is representative of low vehicle speed conditions.
DCO/DCO2 and DCOV/DCO2 ratios are depending on vehicles speed (ex. Popa et al, 2013 ; Xueref-Remy et al, ASTRE, in prep).

## Slide 15
Ammoura et al, ACP 2016
Collaboration + V. Gros, B. Bonsang et la CE team , F. Chevallier, F. Vogel (SatInv), Y. Té, F. Ravetta (QUALAIR), M. Delmotte et al (ICOS-Fr)
PhD work of Lamia Ammoura
QUALAIR – Jussieu Fall 2013 campaign (IPSL Multi-CO2 project)
Characterizing the atmospheric CO2-COV ratios in the Paris open atmosphere

## Slide 16
Good correlation with species related to combustion sources (R2 > 0.8)
Characterizing the atmospheric CO2-COV ratios in the Paris open atmosphere
DCO/DCO2 (ppb/ppm)
7
6
5
4
3
2
1
0
02.2013 05.2013 08.2013 11.2013 02.2014 05.2014
Heating : 2,7 ppb/ppm
Traffic : 7.1 ppb/ppm
Constant ratios, day and night
CO2 source from BB in winter ? (BB = 90 % CO emission estimates in IDF)
Or is the inventory wrong with Residential & tertiary RCO/CO2 ?
PhD work of Lamia Ammoura
Ammoura et al, ACP 2016
New method appropriate for studying signatures of urban domes
Combustion sources speciation difficult because multiple sources for each gas
Spatial and seasonal variability demonstrated using the Megapoli/CO2-MP WINTER campaign dataset
Seasonal disagreement with the AIRPARIF inventory (2010):
Recall from the tunnel campaign:
8,8 ppb/ppm for DCO/DCO2
Rapport DCOV/DCO2
Amplitude du pic de CO2 (fond D enlevé) (ppm)

## Slide 17: CONCLUSION et PERSPECTIVES sur le CO2 en IDF Campagnes récentes et analyses en cours en lien avec la communauté OCAPI Rôle clé du site QUALAIR
Campagne COCOON : tests FTIR LR XCO2 (PI: F.Vogel)
(QUALAIR, GIF, CRETEIL + nord IDF, Mai-juin 2015)
LSCE, KIT-Bremen, LERMA, LISA
Observables: XCO2, CO2, 14CO2
Vogel et al, in prep
Campagne Paris 2030 - OCAPI (PI: I. Xueref-Remy)
(QUALAIR & IDF, fév-avril 2016): Rôle du chauffage au bois?
Collaboration LSCE, LATMOS, LERMA, INERIS
Observables: CO2, CO, 14CO2, d13CO2, carbone suie, lévoglucosan, manosan, COVs, COS, PM et hABL
Xueref-Remy et al, AGU 2016 ; Xueref-Remy et al, in prep
Modélisation inverse (Resp.: G. Broquet)
Optimisation des inventaires d’émissions
LSCE, QUALAIR
Broquet et al, in prep
TCCON-Paris à QUALAIR (PI: Y. Té)
Thèse Dmitry Koshelev: Variabilité de XCO2 sur Paris
Collaboration LERMA, LATMOS, OSU Pytheas
Observables utilisées: XCO2, CO2, hABL
Koshelev et al, in prep
Le réseau de CO2 parisien en 2017 (EIF en construction)
JUS = = QUALAIR

## Slide 18: Merci !
O C P I
La plateforme
d’Observation de la Composition
de l’Atmosphère Parisienne de l’IPSL
Un petit logo pour la plateforme OCAPI?

## Slide 19
Inverse modeling
Echelle urbaine : le projet CO2-Megaparis
CO2-MEGAPARIS / CarboCount City (G. Broquet, F.M. Bréon, F. Chevallier, F. Ciais)
Staufer et al, ACP 2016
Bréon et al, ACP 2015
ECMWF- CHIMERE (2 x 2 km2, 1h)
Postdoctorate work of Vincent Puygrenier
Postdoctorate work of Johannes Staufer

## Slide 20: COCCON

## Slide 21: Publications

## Slide 22
Ammoura et al, ACP 2016
Collaboration + V. Gros, B. Bonsang et la CE team , F. Chevallier, F. Vogel (SatInv), Y. Té, F. Ravetta (QUALAIR), M. Delmotte et al (ICOS-Fr)
PhD work of Lamia Ammoura
Jussieu Fall 2013 campaign (Multi-CO2, PI)
Characterizing the atmospheric CO2-COV ratios in the Paris open atmosphere
Main results (extra-slide available) :
Remarkably, very stable DVOC/DCO2 ratios at low speed turning winds => atmospheric signatures of Paris emissions
Identification of several VOCs from superimposed combustion sources => need more work on VOC analysis (PMF…)
DCO/DCO2 ratio seasonal cycle in disagreement with AIRPARIF inventory:
Wrong ratio for heating? Unknown wood burning CO2 source in Paris ? Wrong airmass footprint?

## Slide 23: Conclusions/ perspectives
PERSPECTIVES
More work must be carried on characterizing and modeling vertical transport above urbanized areas.
Small scale modeling could help to assess the role of fine processes like turbulence on urban CO2 variability.
14C remains today the best tool to separate biospheric fluxes vs FF emissions signals in the CO2 urban plume.
d13C signatures must be better characterized through dedicated studies on fossil CO2 sources & on the biosphere.
The multi-species approach will gain by combining isotopes, VOCs and other tracers of combustion (ex. BC).
URBAN SCALE
Very novative results were gathered from atmospheric approaches to better assess :
  The uncertainties of CO2 bottom-up emission inventories
  The coupling between atmospheric transport processes and CO2 (ex. advection, ABL height dynamics).
Lessons were learned about urban CO2 network design useful for the growing urban research community
Demonstration was given on a potential of atmospheric VOC/CO2 ratios to infer the role of emission sectors.